## Slide 1
Weekly Meeting
25.07.10.
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)
Notes: Weekly meeting 표지

## Slide 2
Goal: Analyzing Latency in Autonomous Drone Navigation via Offboarding
Requirement:
  Understanding the Logic of Autonomous Drone Navigation via Offboarding
  Analyzing Latency at Each Stage of the Process
    MAVROS Communication Flow
  Testing ROS Topics Required for Latency Measurement and Autonomous Navigation
2
Goal

## Slide 3
Analyzing Latency in Autonomous Drone Navigation via Offboarding
3
Intro
onboarding
offboarding

## Slide 4
Analyzing Latency in Autonomous Drone Navigation via Offboarding
4
Intro
non-ROS app
keep-alive message
(offboard mode 유지)
이륙 명령

## Slide 5
On-boarding
Off-boarding
5
Background(Onboarding & Offboarding)
ROS2
ros2 node
message pub
MAVROS
mavros node
DDS to MAVLink
PX4 SITL
hardware 역할
PX4 SITL
hardware 역할
Gazebo
Simulator
PX4: 드론 제어 펌웨어
MAVLink: UAV 통신 protocl
MAVROS: DDS↔MAVLink 변환
Latency 발생
Gazebo
Simulator

## Slide 6
Topic vs Service
6
MAVROS Node
 | Topic | Service
Communication | Publisher-Subscriber | Request-Response
Activation | 지속적인 데이터 | 일회성 명령
목적 | Data Flow | Command (by user)
활용 예시 | 센서, 위치, 상태 | 작업 명령

## Slide 7
7
Background(Offboarding Mechanism)
Node 1
/cmd/arming
Node 2
/cmd/takeoff
Node 3
/cmd/set_mode
Node 4
/cmd/set_posi
Node 5
/cmd/battery
service call
topic pub
Topic 1
/cmd/set_posi
MAVROS
/mavros_node
PX4 SITL
Topic 2
/cmd/state
현재 드론
상태
x: 1.0
y: 1.0
z: 5.0
x: 1.0
y: 1.0
z: 5.0
keep-alive message
(offboard mode 유지)
ROS 2
현재 드론
상태
일회성 명령
지속적인 명령
MAVROS 통신 구조

## Slide 8
MAVROS Node
MAVROS Node 구조
8
MAVROS Node
ROS2
PX4 SITL
Service
Plugin
최종 Queue
Topic
Service
Plugin
Service
Plugin
Service
Plugin
Plugin
Topic
Plugin
Topic
Plugin
Topic
Plugin
지속적인 명령
일회성 명령

## Slide 9
Service 명령: 일회성
  mavros_node.cpp → … → send_message()
Topic 명령: 지속적
  mavros_node.cpp → … → send_message()
최종 queue:
Priority queue 구현하기
  Topic 명령의 Priority 낮추기(mavros package)
  Priority queue 구조로 바꾸기(libmavconn package)
9
MAVROS Node
send_message() 함수 호출 순서대로
topic | topic | topic | service | topic | topic | 

## Slide 10
기존 실험
변경된 실험
10
Experiment
명령 입력
결과 반환
send_message 호출
최종 queue에서 pop

## Slide 11
Thank you
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)