## Slide 1
Weekly Meeting
25.08.01.
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)
Notes: Weekly meeting 표지

## Slide 2
Goal: Analyzing Latency in Autonomous Drone Navigation via Offboarding
Requirement:
  Understanding the Logic of Autonomous Drone Navigation via Offboarding
  Analyzing Latency at Each Stage of the Process
    MAVROS Communication Flow
  Testing ROS Topics Required for Latency Measurement and Autonomous Navigation
2
Goal

## Slide 3
PX4 commander by On-boarding vs Off-boarding
On-boarding
Off-boarding
3
Background
Drone Software
Simulator
Middleware
Drone Software
Simulator
command 생성
command 생성
MAVROS

## Slide 4
Topic vs Service
4
Background
 | Topic | Service
Communication | Publisher-Subscriber | Request-Response
Activation | 지속적인 데이터 | 일회성 명령
Purpose | Data Flow | Command (by user)
example | sensor, position, status | task

## Slide 5
Latency of Service Commands under topic traffic in MAVROS
service call: arming
topic pub: set_position
5
To do
arming
set_position
ROS2
MAVROS
set_position
set_position
set_position
set_position
arming
PX4
keep-alive message
(offboard mode 유지)

## Slide 6
명령 처리 과정
6
명령 처리 과정(Old)
ROS2
libmavconn
MAVROS
router
Queue → PX4
Service
Service
Topic
param
Plugin
Plugin
Plugin
Plugin
send_message()
send_message()
send_message()
send_message()
send_to_lib()
send_to_lib()
최종 Queue에서 명령이 모인다
keep-alive message
(offboard mode 유지)
개별적으로 처리
send_to_lib()

## Slide 7
7
명령 처리 과정(New)
ROS2
libmavconn
MAVROS
router
Queue → PX4
Service
Service
Topic
param
Plugin
Plugin
Plugin
Plugin
send_message()
send_message()
send_message()
send_message()
send_to_pQ()
send_to_pQ()
send_to_pQ()
Priority Queue
우선순위 부여
우선순위 처리
Notes: 1: 간접솔루션 피포큐 밑에 프리어러티 큐를 만들었따. 이때
한계 + 왜 이런방법을 했는지
2: pQ 공부하기(웅기)
3: 명백한 솔류션(립마브콘 큐를 프리어러티 큐로 수정)
왜 어려운지
락걸리고 플로우랑 구조
잘 설명해보자
새로 알게된 정보로 계획

## Slide 8
8
명령 처리 과정(New)
ROS2
libmavconn
MAVROS
router
Queue → PX4
Service
Service
Topic
param
Plugin
Plugin
Plugin
Plugin
send_message()
send_message()
send_message()
send_message()
send_to_pQ()
send_to_pQ()
send_to_pQ()
Priority Queue
send_to_lib()

## Slide 9
Priority Queue code
9
Priority Queue
Old
New
추가된 함수

## Slide 10
Priority Queue 처리 방식
10
Priority Queue
Topic
Service
Service
Topic
Topic
Topic
Topic
Service
Service
Topic
Topic
Topic
주기적으로 일괄 처리

## Slide 11
Priority Queue & libmavconn Queue
11
Priority Queue
PQ
lQ
High
Low
High
Low
High
Low

## Slide 12
Priority Queue & libmavconn Queue
12
Priority Queue
PQ
lQ
High
Low
High
Low
High
Low

## Slide 13
Priority Queue & libmavconn Queue
13
Priority Queue
PQ
lQ
High
Low
High
Low
High
Low
Low
Low
High
Low

## Slide 14
Priority Queue & libmavconn Queue
14
Priority Queue
PQ
lQ
Low
Low
Low
Low
High
Low

## Slide 15
Priority Queue & libmavconn Queue
15
Priority Queue
PQ
lQ
Low
Low
Low
Low
High
Low
Notes: multi level

## Slide 16
Priority Queue & FIFO Queue 출력하기
Priority Queue 처리 방식
  이게 맞나?
command delay 비교: Priority Queue vs FIFO Queue
16
To do

## Slide 17
Thank you
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)