## Slide 1
Weekly Meeting
25.08.07.
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)
Notes: Weekly meeting 표지

## Slide 2
Goal: Analyzing Latency in Autonomous Drone Navigation via Offboarding
Requirement:
  Understanding the Logic of Autonomous Drone Navigation via Offboarding
  Analyzing Latency at Each Stage of the Process
    MAVROS Communication Flow
  Testing ROS Topics Required for Latency Measurement and Autonomous Navigation
2
Goal

## Slide 3
PX4 commander by On-boarding vs Off-boarding
On-boarding
Off-boarding
3
Background
Drone Software
Simulator
Middleware
Drone Software
Simulator
command 생성
command 생성
MAVROS

## Slide 4
Topic vs Service
4
Background
 | Topic | Service
Communication | Publisher-Subscriber | Request-Response
Activation | 지속적인 데이터 | 일회성 명령
Purpose | Data Flow | Command (by user)
example | sensor, position, status | task

## Slide 5
Latency of Service Commands under topic traffic in MAVROS
service call: arming
topic pub: set_position
5
To do
arming
set_position
ROS2
MAVROS
set_position
set_position
set_position
set_position
arming
PX4
keep-alive message
(offboard mode 유지)
delay check!
set_position 명령에 의해
arming 명령이 지연되는 문제를 해결해보자

## Slide 6
명령 처리 과정
6
명령 처리 과정(Old)
ROS2
libmavconn
MAVROS
router
Queue
Topic
Service
param
heartbeat
send_message()
send_message()
function_1()
function_2()
send_to_lib()
send_to_lib()
service_plugin
topic_plugin
param_plugin
heartb_plugin
여기서 모든 명령이 모임
MAVROS 초기 실행시 기본으로 동작하는

## Slide 7
명령 처리 과정
7
명령 처리 과정(New)
ROS2
libmavconn
MAVROS
router
Queue
Topic
Service
param
heartbeat
send_message()
send_message()
function_1()
function_2()
send_to_lib()
send_to_lib()
service_plugin
topic_plugin
param_plugin
heartb_plugin
Priority Queue
우선순위 부여
Service 명령과 Topic 명령은
우선순위를 따른다

## Slide 8
Priority Queue code
8
Priority Queue
Old
New
추가된 함수

## Slide 9
Priority Queue 처리 방식
9
Priority Queue
Topic
Service
Service
Topic
Topic
Topic
ROS2
Topic
Service
com_T
com_T
com_T
libmavconn
Priority Q

## Slide 10
Priority Queue 처리 방식
10
Priority Queue
Topic
Service
Service
Topic
Topic
Topic
ROS2
Topic
Service
com_S
com_T
com_T
com_T
libmavconn
Priority Q

## Slide 11
Priority Queue 처리 방식
11
Priority Queue
Topic
Service
Service
Topic
Topic
Topic
ROS2
Topic
Service
com_S
com_T
com_T
com_T
주기적으로 libmavconn으로 보낸다
libmavconn
Priority Q

## Slide 12
Priority Queue 처리 방식
12
Priority Queue
Topic
Service
Service
Topic
Topic
Topic
ROS2
Topic
Service
com_S
com_T
com_T
com_T
libmavconn
Priority Q
정렬된 순서에 맞춰서 실행된다

## Slide 13
Priority Queue 처리 방식
13
Priority Queue
ROS2
Topic
Service
Priority Q

## Slide 14
구현 방식의 난이도가 낮다
14
왜 이런 방식을 선택했는가?
ROS2
libmavconn
MAVROS
router
Queue
Topic
Service
param
heartbeat
send_message()
send_message()
function_1()
function_2()
send_to_lib()
send_to_lib()
service_plugin
topic_plugin
param_plugin
heartb_plugin
Priority Queue
여기만 수정하면 된다!

## Slide 15
우선순위가 보장된다
15
왜 이런 방식을 선택했는가?
PQ
libmavconn
High
Low
High
Low
High
Low

## Slide 16
우선순위가 보장된다
16
왜 이런 방식을 선택했는가?
PQ
libmavconn
High
Low
High
Low
High
Low
Low
High
Low
High
Low
C++ Priority Queue: heap 기반
 | 삽입 | 삭제
PQ | O(logN) | O(logN)
Q | O(1) | O(1)
FIFO Q

## Slide 17
우선순위가 보장된다
17
왜 이런 방식을 선택했는가?
PQ
libmavconn
High
Low
High
Low
High
Low
Low
High
Low
High
Low
PQ에 명령이 들어오는동안
libmavcon는 이미 비어진다

## Slide 18
Service와 Topic 외에 다른 msg가 있다
18
어떤 문제가 있나요?
ROS2
libmavconn
MAVROS
router
Queue
Topic
Service
param
heartbeat
send_message()
send_message()
function_1()
function_2()
send_to_lib()
send_to_lib()
service_plugin
topic_plugin
param_plugin
heartb_plugin
Priority Queue
실행 중에 간헐적으로 msg가 pub됨

## Slide 19
Service와 Topic 외에 다른 msg가 있다
19
어떤 문제가 있나요?
PQ
libmavconn
High
Low
High
Low
High
Low
Low
High
Low
High
Low
ROS2
Topic
Service
param
heartbeat
com_H
PQ에서 lQ로 보내는 주기에 따른 delay가 발생
우선순위를 보장하기 위해
전체 시스템이 느려진다
다른 msg 종류가 몇 개나 더 있는지는 잘 모름
왜? 언제? 무슨 이유로? 실행되는지 모름

## Slide 20
libmavconn Queue → Priority Queue
20
To do
ROS2
libmavconn
MAVROS
router
Queue
Topic
Service
param
heartbeat
send_message()
send_message()
function_1()
function_2()
send_to_lib()
send_to_lib()
service_plugin
topic_plugin
param_plugin
heartb_plugin
Priority Queue로 바꾸자
libmavconn으로 명령을 보내는 모든 함수 파악하기
libmavconn→PX4 전송 방식(mutex lock)
[ICCAS 2022]

## Slide 21
Thank you
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)