## Slide 1
Weekly Meeting
25.05.12.
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)
Notes: Weekly meeting 표지

## Slide 2
Goal: Analyzing Latency in Autonomous Drone Navigation via Offboarding
Requirement:
  Understanding the Logic of Autonomous Drone Navigation via Offboarding
  Analyzing Latency at Each Stage of the Process
  Testing ROS Topics Required for Latency Measurement and Autonomous Navigation
2
Goal

## Slide 3
Onboarding: PX4 내부에서 직접 실행
Offboarding: 외부 터미널
3
Onboarding & Offboarding
ROS2
protocol: DDS
PX4
protocol: MAVLink
Gazebo
simulator
MAVROS
Bridge
PX4
protocol: MAVLink
Gazebo
simulator
<PX4 shell>
command
<Terminal>
ros2 run node
PX4: 드론 제어 펌웨어
MAVLink: UAV 통신 protocl
MAVROS: DDS↔MAVLink 변환

## Slide 4
Onboarding: 4ms~8ms
Offboarding: 100ms~2000ms
ROS2→MAVROS→PX4→MAVROS→ROS2
4
Latency: Onboarding vs Offboarding
ROS2
MAVROS
Bridge
PX4
<PX4 shell>
command
<Terminal>
ros2 run node
PX4
/mavros/state
/mavros/cmd/arming

## Slide 5
MAVROS
  Single node(/mavros/mavros_node)
  Plugin 기반(/mavros/setpoint, /mavros/localposition, /mavros/velocity…)
  중앙 queue
Latency 원인: 중앙 queue에서 명령이 밀림
  Plugin 최적화: 사용하지 않는 plugin 종료
  QoS 조정: reliable → besteffort(reliable의 경우 손실 시 명령 재전송)
  명령 주기 조정: 0.01s → 0.1s(PX4 명령 처리 시간)
5
Latency test: MAVROS
takeoff | takeoff | takeoff | state | position | takeoff | takeoff | takeoff | state | position
Offboard mode: takeoff(0.01s)
/mavros/state(0.1s)
/mavros/position (0.1s)
+ 기본으로 실행되는 plugin

## Slide 6
Offboard 명령 주기 조정에 따른 latency
  1/s: 509.6ms
  10/s: 1128.6ms
6
Latency test: 명령 주기 조정
Chart: 

## Slide 7
실행중인 plugin에 따른 latency(rate: 1/s)
  1/s: 509.6ms
  Many plugin: 1351.1ms
7
Latency test: Plugin 최적화
Chart: 

## Slide 8
Latency 원인: 중앙 queue에서 명령이 밀림
  Plugin 최적화: 사용하지 않는 plugin 종료
  QoS 조정: reliable → besteffort(reliable의 경우 손실 시 명령 재전송)
  명령 주기 조정: 0.01s → 0.1s(PX4 명령 처리 시간)
  Priority: MAVROS process
  Muti-thread: Callback group
8
improvement
dds | dds | dds | dds | dds
mavlink | mavlink | mavlink |  | 
ROS2
2. MAVROS
Y. Yang and T. Azumi, "Exploring Real-Time Executor on ROS 2," 2020 IEEE International Conference on Embedded Software and Systems (ICESS), Shanghai, China, 2020, pp. 1-8

## Slide 9
9
Latency test
우선순위에 따른 Latency
명령 주기에 따른 Latency
Chart: 우선 순위에 따른 Latency
Chart: 명령 주기에 따른 Latency

## Slide 10
10
Latency test
우선순위에 따른 Latency
명령 주기에 따른 Latency
Chart: 

## Slide 11
Thank you
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)