## Slide 1
Weekly Meeting
25.06.20.
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)
Notes: Weekly meeting 표지

## Slide 2
Goal: Analyzing Latency in Autonomous Drone Navigation via Offboarding
Requirement:
  Understanding the Logic of Autonomous Drone Navigation via Offboarding
  Analyzing Latency at Each Stage of the Process
  Testing ROS Topics Required for Latency Measurement and Autonomous Navigation
2
Goal

## Slide 3
On-boarding
Off-boarding
3
Background(Onboarding & Offboarding)
ROS2
ros2 node
message pub
MAVROS
mavros node
DDS to MAVLink
PX4 SITL
hardware 역할
PX4 SITL
hardware 역할
Gazebo
Simulator
PX4: 드론 제어 펌웨어
MAVLink: UAV 통신 protocl
MAVROS: DDS↔MAVLink 변환
Latency 발생
Gazebo
Simulator

## Slide 4
4
Background(Offboarding Mechanism)
Node 1
/cmd/arming
Node 2
/cmd/takeoff
Node 3
/cmd/set_mode
Node 4
/cmd/set_posi
Node 5
/cmd/battery
service call
topic pub
Topic 1
/cmd/set_posi
MAVROS
/mavros_node
PX4 SITL
Topic 2
/cmd/state
현재 드론
상태
x: 1.0
y: 1.0
z: 5.0
x: 1.0
y: 1.0
z: 5.0
keep-alive message
(offboard mode 유지)
ROS 2
현재 드론
상태

## Slide 5
mavros_node.cpp
/plugins/command.cpp
/plugins/0000.cpp
/lib/mavros_router.cpp
/lib/mavros_uas.cpp
/libmavconn
5
MAVROS Node
ROS2 Node
PX4 SITL
ROS2 Node
ROS2 Node
ROS2 Node
ROS2 Node
MAVROS Node
Queue 관리
Protocol 변환
Plugin 관리
Message routing
ROS2 Topic
ROS2 Topic
ROS2 Topic
ROS2 Topic
ROS2 Topic

## Slide 6
ros2 service call /mavros/cmd/arming
mavros_node.cpp
command.cpp
  arming_cb()
  send_command_long_and_wait()
  commande_long()
mavros_uas.cpp
  msg_set_target()
  send_message()
6
command 실행 과정

## Slide 7
Queue 길이: 1000
7
Queue 구조
Plugin 별 Queue
Command
Plugin 2
Plugin 3
libmavconn Queue
command
set position
Set position
Mavlink
send_message() 호출 순서

## Slide 8
libmavconn 패키지에 있는 코드 확인하기
최종 Queue를 priority queue로 변경
  high priority: service call
  low priority: 그 외
목표: 실제로 되는지 안 되는지만 확인해보기
uXRCE-DDS communication
8
To do

## Slide 9
Thank you
Advisor : Hoon Sung Chwa
Dept of Electronic Engineering & Computer Science, DGIST
Real-Time Computing Lab
Moonyoung Choi (cmy021205@dgist.ac.kr)